## Slide 1: Assignment- part-2
Opportunities of MVNO by Femtocell Deployment

## Slide 2: Outline of the Presentation
MVNO and Femtocell
Present scenario
Strategies to be thought for deployment of femtocell by MVNO
Deployment set-ups, based on the roles of the actors in the mobile supply chain ;
Opportunity & Risk based on role of the actors
Structure of business model
outcome

## Slide 3: Definition
Cellphone
Femtocell
Internet through a broadband router
Mobile operators’ network
Notes: MVNO (certain): Provides mobile services to its subscribers, with whom it has direct contact and for whom it takes care of the customer relationship management, the branding,
marketing and sales. The MVNO does not possess a license nor does it own macrocell infrastructure. Therefore, the MVNO will need to use others’ access networks (either femtocells, macrocells or a combination) and have an MNO’s authority (on a contractual basis and with likely compensation) to operate in its licensed spectrum.
Cognitive Service Provider (optional): Can provide services that avoid interference and enable cognitive sharing of the same (licensed) spectrum resource. When contracted, this actor can its cognitive elements (e.g. sensing engines and/or database) to allow MVNOs and MNOs to share the same spectrum resource without any interference, while making use of both macrocells and femtocell.

## Slide 4: Present Scenario
MVNO
Problem
Licensed spectrum scarce of MVNO;
Lack of authority;
Customer needs ( coverage, signal strength)
Europe: deployment with 3G, 4G or up
Asian: still 2G, 3G
Femtocell
short-range, low-power, low-cost cellular base stations
It is expected that femtocells will gain
importance in the future and Cisco estimates that by 2016,
“over 3.1 exabytes of mobile data traffic will be offloaded to the fixed network by means of dual-mode devices and femtocells each month”
* Not only popularize 3G and MVNO services but also in wireline services
Notes: Licenced spectrum scarcity: due to mobile data crunch. It is expected that by 2016, the monthly global mobile data traffic will surpass 10 exabytes, Solution: Many solutions, including Cognitive Radio, driven by cognitive enablers such as spectrum sensing , the cognitive
pilot channel and the geolocation database , have been proposed as solid solutions to alleviate the spectrum scarcity by making more efficient use of the limited spectrum.
Femto: Used to serve small area

## Slide 5: Strategic points for deploying femtocell by MVNO
Actor?
Configuration?
Projection
MVNO/MNO/MVNE/
Open or Closed access?
Subscriber no
Device needed to coverage
Notes: Which actor in the mobile ecoystem can be responsible
for the deployment of the femtocells and the cognitive
elements?
o Should the femtocells be configured to allow open
access or closed access ?
o What is the optimal number of subscribers per
femtocell?
o How much femtocells are needed, provided a given
amount of subscribers?
Open or closed access: One femtocell can be used to serve multiple subscibers, which is referred to as open access, but it can also be used to serve just one particular subscriber per femtocells, which is referred to as closed access. If an MVNO wants to serve mobile services to its clients, the choice with regard to the type of access is also part of the strategic plan for femtocell deployment.

## Slide 6: Deployment set-ups, based on the roles of the actors in the mobile supply chain
Notes: In mobile markets, such niche segments are often served by MVNOs (mobile virtual network operators), as they can focus on specific targeting, using customized marketing (communications) and sales, while offering segment-specific mobile offers (in this case potentially including high bandwidths and large data limits).
1. MVNO deployment: In an MVNO deployment set-up, the MVNO is responsible for the traditional MVNO roles such as providing value added services, performing back office operations, formulate offers and take care of distribution, marketing and sales. However, apart from these standard MVNO-specific roles, the MVNO will also have to invest in femtocells and cognitive elements. For an MVNO this entails very high costs and thus high risks. However, this set-up also brings very high
rewards because the MVNO can lock-in customers (by
functioning as exclusive operator to work with the femtocells),
it does not need to share the femtocells and can thus provide
higher bandwidths, which in turn allows for higher pricing.
2. MVNE deployment
3. MNO deployment- MVNO is only responsible for the traditional MVNO roles such as providing value added services, performing back office operations, formulate offers and take care of distribution, marketing and sales.MVNO will deprive from wholeslae power. The new functions (the cognitive control and rollout of
femtocells as access network) are taken up by the MNO.
Similar to the MVNE deployment, this lowers the risks for the
MVNO. However, an additional risk, compared to the MVNE
deployment is the fact that an MVNO will no longer benefit
from wholesale pricing, but would need to negotiate directly
with an MNO to acquire available licensed spectrum. This
increased risk also brings additional rewards as the entry
barriers for other MVNOs become higher, lowering
competition. As a result, the MVNO can set higher prices,
resulting in higher MVNO rewards as compared to the
rewards when opting for an MVNE deployment.
4. MVNO deployment with third party Cognitive Service Provider: A last set-up is the MVNO deployment with third party Cognitive Service Provide r (CSP). Apart from its traditional functions, the MVNO also invests in the rollout of femtocells. It acquires spectrum by directly negotiating with the MNO, but in this case, the MVNO also appoints a third party entity, the CSP, which invests in cognitive elements (e.g. sensing engines or database) and performs the cognitive controls in order to make better use of the MNO’s spectrum, by avoiding harmful interference (between multiple users in the samefrequency bands), enabling seamless handover and ultimately achieving overall network capacity gains. In this deployment, the MVNO is less dependent on the cooperation of the MNO as it will no longer need to utilize the MNO’s femtocells.
However, deploying the MVNO’s own femtocells would
result in much higher risks, given the substantial investment.
On the other hand, higher rewards for the MVNO can also be
expected as the MVNO could profit from limited competition
and customer lock-in (if the MVNO’s customers want to leave
the MVNO for another operator, they would have to get a new
femtocell).

## Slide 7: Opportunity & Risk
Reward
MVNO/ MVNO+CSP Reward(Customer lock in, revenue and negotiation power)
MNO/ MVNE Reward(Customer lock in, revenue and negotiation power)
Risk
MVNO/ MVNO+CSP Risk(CAPEX, OPEX, Complexity)
MNO/ MVNE Reward(Customer lock in, revenue and negotiation power)

## Slide 8: Structure of Business Model
Key Partners
Key activities & Key Resources
Value Proposition
Customer Segments
Cost Structure
Revenue Model
Customer Relationship and Channel
Notes: A business model describes the rationale of how an organization creates, delivers, and captures value in economic, social, cultural or other contexts. The process of business model construction is part of business strategy.
Key partner: who will be the key partner?
Key activities: what have to do for value proposition?
Value proposiiton: good signal, capacity
CRM: how to reach cutomers
Cost Structure: installation cost of femtocell,

## Slide 9: Outcome of business model: Inverse MVNO?
It will be collaborative business model
Business opportunity for MVNO; business strategy execution;
Identify new services by service providers to end users;
QoS ensure
Identify the different entity in value chain
ARPU and Capex-Opex (?)

## Slide 10: References
Shared Smallcell Networks:Multi-Operator or Third Party Solutions – ?Or Both? Jan Markendahl, Amirhossein Ghanbari, Wireless@KTH, Royal Institute of Technology, Electrum 229, SE-16440, Kista, Sweden
Femtocell deployment strategies for MVNOs enabled by cognitive sharing
Matthias Barrie, Anand Raju, Simon Delaere, IBBT-SMIT, Vrije Universiteit Brussel Pleinlaan 9, 1040 Brussel, Belgium, Gaston Crommenlaan 8, 9050 Gent, Belgium
Femtocell Mass Deployment: Indian Perspective, Dr. S.S. Prasad1, Rithika Baruah2, Department of Electronics and Communication, National Institute of Technology.
A Femtocell Business Model:The BeFEMTO view, Jean-Baptiste Vezin1, Lorenza Giupponi2, Alexander Tyrrell3,Emilio Mino4, Brzozowy Miros􀃡aw5